## Slide 1: PickyRTL

## Slide 2: Project Background
Research Project Title: RTL-level Secure Coding against Hardware Attacks
  The main goal is to implement detection algorithms for CWEs
Register Transfer Level (RTL)
  Part of the hardware design process
  Is a hardware description abstraction
  Defines digital circuit behavior in terms of data flow between registers
  Is written in a Hardware Description Language (HDL)
    Verilog, SystemVerilog, VHDL
Notes: Combinational = pure function of inputs (no clock, no memory) (outside of always)
Sequential = depends on history (uses clock, has registers) (always @(posedge clk) begin)
Why RTL? – Human-readable, which enables static analysis, catching weaknesses earlier, is easier and less costly to fix
System specification – architectural requirements
RTL – coding the chip design, describes data movement and logic operations between registers, what the circuit does
Logic synthesis – gates and netlists, simulation of code and analysis of timing/functionality
Physical design – layout of the chip
Fabrication - silicon

## Slide 3: What is CWE?
Stands for Common Weakness Enumeration
List of common hardware and software weakness types
Weakness – a condition that under certain circumstances, could contribute to the introduction of vulnerabilities
Selected 4 CWEs for static analysis detection
  CWE-1245
  CWE-1233
  CWE-226
  CWE-1431
Notes: Vulnerability – an exploitable flaw that can be exploited in a deployed system
The CWEs were selected based on their ability to be detected through static analysis and their relevance in the 2021 MIHW list and 2025 MIHW list
Provides a standardized framework for identifying, categorizing, and preventing security issues during development
It is maintained by MITRE corporation

## Slide 4: Detection Overview
Notes: Parse HDL files with HDL convertor into a JSON AST format
Then we extract relevant data (FSM, cryptographic modules, security critical registers) from the AST
Then we run through the detection algorithms and receive a vulnerability report

## Slide 5: CWE-1245: Improper Finite State Machines (FSMs) in Hardware Logic
FSMs are commonly used in hardware logic for secure data operations, security state, and other functionality
Vulnerable Patterns
  Deadlocks
  Unreachable states
  Incomplete state coverage
Consequences
  System could enter a deadlocked state
  Bypass security authentication
  Unpredictable system behavior
Detection
  Incomplete state coverage?
  Unreachable states?
  Deadlock states?
Notes: The patterns can lead to consequences. The example shows an FSM with incomplete state coverage. The state variable ‘user_input’ has 4 possible values because it is 2 bits long. There are originally only 3 defined states. If ‘user_input’ had a value of 2’h3 the system would enter an unpredictable state and could possibly be exploited
Could be exploited through fault injection attacks
2 – 2 bit width
H – hexadecimal
3 - value

## Slide 6: CWE-1233: Security Sensitive Hardware Controls with Missing Lock Bit Protection
Lock Bit – A hardware mechanism that prevents modification of registers after they have been set
Security-critical registers should be protected with lock bits
Consequences
  Security policies could be bypassed if access controls are modified
  Keys could be overwritten
Detection
  Identify the lock bit
  Gather security-critical registers
  Are assignments made to the registers unprotected?
Notes: Security-critical registers – boot configurations, control settings, debug interface controls, keys
The example shows a key in some cryptographic module that should be protected with lock bit, but is not.

## Slide 7: CWE-226: Sensitive Information in Resource Not Removed Before Reuse
Registers often store sensitive information such as cryptographic keys, authentication tokens, etc.
If the registers aren’t cleared after being used, the data persists and can be accessed by subsequent operations
Consequences
  Cryptographic key leakage to unauthorized process
  Sensitive data could be accessed by untrusted parties
Detection
  Identify the reset signal
  Gather registers that need to be reset
  Are the registers properly reset?
Notes: The example shows a hashing module where the input message is not cleared. If this is not cleared then the unhashed input message will remain on that register and could be accessed by an untrusted party/process

## Slide 8: CWE-1431: Driving Intermediate Cryptographic State/Results to Hardware Module Outputs
Cryptographic modules often involve intermediate results between rounds of encryption
These results should remain internal and not be exposed to output ports
Consequences
  Intermediate results could be observed by untrusted parties through side channel attacks
Detection
  Identify the cryptographic module output
  Find any registers containing intermediate results
  Are intermediate results assigned to the module output before checking if the result is valid?
Notes: Intermediate results can give attackers a chance to decipher the original message
The result in the example should not be driven to the data_o output before the result is actually valid

## Slide 9: Questions?