## Slide 1
PickyRTL: A Static Analysis Tool for Detecting
Hardware CWEs at Register-Transfer Level
John Parks
Advisor: Dr. Boyang Wang
Background
Results
What is CWE?
Future Work
Detection Algorithms
CWE | # Vulnerable Components | TP | FP | FN | Precision | Recall
CWE-1245 | 9 | 9 | 0 | 0 | 100.0% | 100.0%
CWE-1233 | 30 | 10 | 9 | 11 | 67.9% | 63.3%
CWE-226 | 31 | 21 | 1 | 10 | 95.5% | 67.7%
CWE-1431 | 10 | 10 | 0 | 0 | 100.0% | 100.0%
Total | 80 | 59 | 10 | 21 | 85.5% | 73.8%
Common Weakness Enumeration (CWE)
Community-developed list of common software and hardware weaknesses that could lead to vulnerabilities
Four CWEs selected for detection:
CWE-1245: Improper Finite State Machines (FSMs) in Hardware Logic
CWE-1233: Security-Sensitive Hardware Controls with Missing Lock Bit Protection
CWE-226: Sensitive Information in Resource Not Removed Before Reuse
CWE-1431: Driving Intermediate Cryptographic State/Results to Hardware Module Outputs
CWE-1245 Detection
Identify the state variable for FSM
Convert assignments to the state variable into FSM transitions
Search for
  Incomplete State Coverage
  Unreachable States
  Deadlock States
CWE-1233 Detection
Identify lock bit registers
Identify security-sensitive registers
Gather assignments for each security-sensitive register
Ensure each assignment is protected with the lock bit
CWE-226 Detection
Identify reset signals
Identify sensitive registers that need to be reset
Ensure there is an assignment that resets the register within a conditional containing the reset register
CWE-1431 Detection
Identify cryptographic modules
Identify the output wire containing the result
Ensure assignments driven to the output wire are only made when the result is valid
Evaluated on a dataset of 39 Verilog and System Verilog files
Design Specification
RTL Design
Synthesis
Gate Level Design
Layout
Register Transfer Level (RTL) design is a stage in the digital circuit design process that describes the behavior and structure of a system. It defines how data moves between registers and the operations performed on that data. RTL designs are written using hardware description languages (HDLs) such as Verilog, SystemVerilog, or VHDL. Because RTL is expressed as code, it can be analyzed using static analysis techniques.
We are actively working to improve PickyRTL:
Creating a larger dataset
Improvements to each CWE detection algorithm
Extending coverage to additional CWEs
Limitations
References
module crypto (input clk, input data_i, output data_o);
reg result, result_valid;
always @(posedge clk) begin
//…cryptographic operation
end
assign data_o = result;
endmodule
module hash_msg (input clk, input rst, input msg, output hash);
always @(posedge clk) begin
if (rst) begin
hash = 0
// msg never cleared
end
//…hashing logic
end
endmodule
module unprotected_key (input clk, input reglk, input data);
reg key0, key1;
always @(posedge clk) begin
key0 = data;
key1 = reglk ? key1 : data;
end
endmodule
module fsm (input clk, input x);
reg [1:0] state;
always @(posedge clk) begin
case (state):
0: state = 2;
1: state = 1;
2: state = x ? 1 : 3;
3: state = 0
endcase
end
endmodule
Hardware vulnerabilities cannot be fully fixed with software patches or microcode updates alone. They often require physical modifications to the chip itself, driving up costs and leaving systems exposed for longer periods. Meltdown and Spectre demonstrated this by exploiting speculative execution in processors to steal sensitive data and affected nearly every device on the market. This is why catching vulnerabilities before fabrication is critical. The perfect time for that is during RTL design.
SPECTRE
Limited Dataset Size
While we have preliminary results from our dataset, a larger, more diverse dataset would enable a more comprehensive evaluation.
Identifying Security-sensitive Registers
With static analysis, we only have a limited amount of context about the module and the defined registers. Without more semantic context, it is hard to identify security-sensitive registers
Name Matching
Identifying cryptographic modules, reset signals, and lock bits with name matching works for conventional names. However, this technique breaks down when non-conventional names are used
Strong performance for CWE-1245 & CWE-1431 where weaknesses appear in structural patterns
Weaker performance for CWE-1233 & CWE-226 where more semantic context is required
Notes: Font Sizes:
Title: 96
Names: 60
Section Headings: 54
Body text: 36
Figure Captions: 24